## Slide 1
INTRODUCTION TO microcontrollers
PLAN DE FORMACIÓN EN LENGUAS EXTRANJERAS 2017
IN-57 Technology for ESO: Contents and Strategies
By Marta Gandia Marcilla

## Slide 2: DESCRIPTION
The aim of this project is to compare different microcontrollers through a practical workshop
It will be used to introduce the lesson in the last quarter of the 3rd year of ESO.

## Slide 3: OBJECTIVES:
Analyse the working process of microcontrollers
Analyse programming instructions
Design electronic circuits
Learn to write code and upload it to the board
Test and check if it works correctly

## Slide 4: Warm up questions
Give the names of some electronic devices in your house ?
Do you know how they are controlled?
Do you think the controller is large or small ?

## Slide 5: Microcontrollers. Definition
A microcontroller is a tiny or small computer present in a single integrated circuit which is dedicated to perform one task and execute one specific application.
It includes a memory, programmable input/output peripherals, as well as a processors.

## Slide 6: Microcontroller types

## Slide 7: BOARD COMMUNICATION:ARDUINO IDE
https://www.arduino.cc/en/Main/Software

## Slide 8: BOARD COMMUNICATION:ARDUINO Principal instructions
Declaring libraries. ex. LiquidCrystal lcd(12, 11, 5, 4, 3, 2);
Declaring variables: int, char, float, double…
SETUP () AND LOOP () functions
Instructions: digitalWrite () command to turn the pins HIGH or LOW.
pinMode()
Delay()

## Slide 9: BOARD COMMUNICATION:BITLOQ
BITLOQhttp://bitbloq.bq.com/#/howitworks

## Slide 10: BOARD COMMUNICATION:BITLOQ
http://bitbloq.bq.com/#/bloqsproject

## Slide 11: BOARD COMMUNICATION: IMAGINA ANDROI
http://www.picaxe.com/

## Slide 12: IMAGINA ANDROI PROGRAM

## Slide 13: PRACTICE 1: COMPUTERS WORKSHOP
Goal: Control a servomotor with a potentiometer and compare 2 boards
Criteria:
Using bq and
Arduino uno boards
Follow the steps
Teams of 2-3 people
Constraints:
Must incorporate the materials provided
Must be programmed in each platform
Time to build: 2 sessions

## Slide 14: Electronic components
Breadboards
LCD displays
Servo-motors
Resistors
Potentiometers
LEDS
Sensors
Cables

## Slide 15: Steps using the Arduino UNO board
You start openning TinkerCAD and design the circuit
Later , please, assemble all the compenents between the breadboard and Arduino UNO board

## Slide 16: Steps using the Arduino UNO board (2)
Now open the Arduino program
Connect the board to the computer
Write the code from the next page
Test: If you move the potentiometer, the servo motor speeds up it velocity ?
ADDITIONAL ACTIVITY:Include a led controled by the potentiometer to blink at the same speed.

## Slide 17: CODE SOLUTION
#include <Servo.h>
Servo myservo; // create servo object to control a servo
int potpin = 0; // analog pin used to connect the potentiometer
int val; // variable to read the value from the analog pin
int sensorPin = A0; // select the input pin for the potentiometer
int ledPin = 13; // select the pin for the LED
int sensorValue = 0; // variable to store the value coming from the sensor
void setup() {
myservo.attach(9); // attaches the servo on pin 9 to the servo object
// declare the ledPin as an OUTPUT:
pinMode(ledPin, OUTPUT);
// initialize digital pin 13 as an output.
pinMode(10, OUTPUT);
}

## Slide 18: CODE SOLUTION (2)
void loop() {
digitalWrite(10, HIGH); // turn the LED on (HIGH is the voltage level)
delay(100); // wait for a second
digitalWrite(10, LOW); // turn the LED off by making the voltage LOW
delay(100); // wait for a second
// read the value from the sensor:
sensorValue = analogRead(sensorPin);
// turn the ledPin on
digitalWrite(ledPin, HIGH);
// turn the ledPin off:
digitalWrite(ledPin, LOW);
// stop the program for <sensorValue> milliseconds:
delay(sensorValue);
val = analogRead(potpin); // reads the value of the potentiometer (value between 0 and 1023)
val = map(val, 0, 1023, 0, 180); // scale it to use it with the servo (value between 0 and 180)
myservo.write(val); // sets the servo position according to the scaled value
}

## Slide 19: Steps using the bq board:
Now, go to bitloq bq
Connect the board to the computer
Assemble the components (picture below)

## Slide 20: Steps using the bq board (2):
Simulate the circuit, bitloq simulator (picture bellow)
Test: When you move the potentiometer, the servo motor speeds up it velocity ?
ADDITIONAL ACTIVITY: Include a LED controlled by the potentiometer to blink at the same speed.

## Slide 21: Debrief questions:
Did you like this workshop?
What did you learn while working on these microcontrollers?
Which board would you prefer to use?
Which of them do you find easier to use?
And which one do you find more complex?

## Slide 22: RUBRIC DESCRIPTION
GRADE POINTS | POOR 1 | FAIR 2 | GOOD 3 | VERY GOOD 4
CIRCUIT DESIGNS- SIMULATION | Completed some of the steps of the designs and simulation | Completed most of the steps of the designs and simulation | Completed each step of the designs and simulation | Completed perfectly each step of the designs and simulation
CIRCUIT CONSTRUCTION | The circuit has some of the electronic components | The circuit has most of the electronic components | The circuit has each electronic components | The circuit has been perfectly assembled with the addional tasks
COMPLETION | Completed some of the work | Completed most of the work | Work completed | Perfectly completed work
GROUP WORK/ COLLABORATION | Rarely works with all team members | Occasionally works with all team members | Works with all team members | Works pretty well with all team members

## Slide 23: RUBRIC TEMPLATE
GRADE POINTS | POOR 1 | FAIR 2 | GOOD 3 | VERY GOOD 4
CIRCUIT DESIGNS- SIMULATION |  |  |  | 
CIRCUIT CONSTRUCTION |  |  |  | 
COMPLETION |  |  |  | 
GROUP WORK/ COLLABORATION |  |  |  |